## Slide 1: Coplane retrieval of airborne radial velocities for Hurricane Katrina (2005)
Christopher Melhauser
Group Meeting
December 11, 2013

## Slide 2: Coordinated Coplanar Scanning
Armijo (1969):
  Proposed determining u, v, w components of wind
    Two Doppler radars
    mass continuity equation (local variations and advection negligible)
    Assumption: Vertical fall speed of hydrometeors known
Figure 1: Armijo (1969)
Figure 1: Miller and Strauch (1974)
Lhermitte and Miler (1970)
  Proposed the COPLAN scanning technique
Miller and Strauch (1974)
  Described technique and algorithm in detail
Chong and Testud (1983)
  Described variational techniques to solve integration errors caused by boundary conditions
Chong and Testud (1996)
  Described airborne coplane technique and error estimates
Notes: Armijo (1969):
  Using an analytical solution to solve for w.
  Use cylindrical coordinates to transform the mass continuity into a simpler partial differential equation.
  Assume at z=0, w=0 for boundary condition
Lhermitte and Miler (1970):
  Proposed at 14th Radar Conference
Miller and Strauch (1971):
  Provided case study of snowstorm in Boulder, CO
Chong and Testud (1983):
  Boundary conditions extremely important when integrating mass continuity
  Large uncertainty in w-component
    Doppler radars usually operate at low elevation angle, which implies the contribution of W to the observed radial velocity is poor
    Radars actually observe the radial velocity of the hydrometeors
Chong and Testud (1996):
  - Use anelastic continuity equation expressed in cylindrical coordinates.

## Slide 3: Coplane Geometry - BC
Figure 1: Adapted from Miller and Strauch (1974)
Baseline
Radar 1
Radar 2
+x
+y
z
Zb
Zt
Integrate mass continuity to solve mean vertical wind
  Errors amplify exponentially with height
    Biases in surface BC (i.e. orography)
BC assumptions:
  W=0 at Zb
  W=vt at Zt
Proposed solutions:
  Integrate from storm top
  Constrain height integrated divergence (Ziegler, 1978)
  Constraining direct estimates of 3D wind field to satisfy continuity (Ray et al., 1980)
  Use variational technique to adjust error of ground level, i.e. floating BC (Chong and Testud, 1983)
What can pure geometric retrieval reveal about large-scale hurricane structure?
Can assimilation of these observations improve analyses of TC’s?
Notes: Chong and Testud (1983)

## Slide 4: Coplane Geometry - Airborne
Performed in cylindrical coordinates
Use fore and aft Doppler radar scans to retrieve mean wind components parallel and perpendicular to flight track on horizontal plane
  Since the aircraft is moving forward, each antenna actually prescribe a helical scan  Assume each fore/aft scan taken at the same time
Figures 1 & 2: Chong and Testud (1996)
760 m**
* Assuming tilt angle of 20o from zenith
** Assuming 10 scans per minute at with plane speed of 130 m s-1
~ 1 km*
Notes: Assume 130 m s-1 with 10 scans per minute (i.e. 6 seconds between forward and back scan)
Assume straight line flight track and constant altitude
  Pitch, yaw, and roll of aircraft already accounted for in radar data

## Slide 5: Coplane Geometry - Airborne
All values of a:
  Unambiguously define mean wind component along flight track:
a = 0o
  Unambiguously define mean horizontal wind component perpendicular to flight track:
a = 90o
  Unambiguously define mean precipitation fall speed
a
r
s
r
Beam 1 = fore
Beam 2 = aft

## Slide 6: Coplane Geometry
Assume constant snapshot in time
  10 seconds between fore/aft  use 20 scans (10 fore/10 aft)  2 minutes
  Advection ignored
Distance from aircraft constrained by geometry and time assumption
  Further distance  requires additional fore/aft scans  reduces confidence in retrieved wind speed
Quality control very important
b+1
f+2
f+1
f
f-1
f-2
b+2
b
b-1
b-2
s
r
f = forward scan
b = backward scan
Min: ~1 km
Max: ~41 km

## Slide 7: Flight Leg 2018-2058

## Slide 8: Flight Leg 2018-2058
RMSEstarboard = 4.69 m s-1
RMSEport = 4.44 m s-1
[m s-1]
Coplane Retrieval (Altitude: ~2.8 -3.1 km)
Dual Doppler
(Altitude: 3.0 km)
Flight Level
~1 km coplane retrieved WS
Flight Level WS / ~1 km coplane retrieved WS Departure

## Slide 9: Katrina Composite 1900-2253
[m s-1]
Need to time shift flight legs for comparison
Not apples to apples comparison; altitude changes +/- 700 m along flight leg

## Slide 10: What is next?
Additional QC on retrieved wind velocity, augmented by flight level data
Additional comparison with flight level in-situ observations
Compare coplane retrieval with Dual-Doppler analyses generated at HRD from same radar data
Time shift observations to build composite
Quantify errors in coplane retrieval
  random errors for retrieved vr and vs winds not independent
Assimilate into WRF/COAMPS and compare with SO data

## Slide 11: Selected References
Armijo, L., 1969: A Theory for the Determination of Wind and Precipitation Velocities with Doppler Radars. J. Atmos. Sci., 26, 570–573.
Chong, M., J. Testud, 1983: Three-Dimensional Wind Field Analysis from Dual-Doppler Radar Data. Part III: The Boundary Condition: An Optimum Determination Based on a Variational Concept. J. Climate Appl. Meteor., 22, 1227–1241.
Chong, M., and J. Testud, 1996: Three-dimensional air circulation in a squall line from airborne dual-beam Doppler radar : a test of coplan methodology software, J. Atmos. Oceanic Technol. 13, 36-53.
Lhermitte, R. M., and L. J. Miller, 1970: Doppler radar methodology for the observations of convective storms. Preprints 14th Radar Meteorology Conf., Tucson, Amer. Meteor. Soc., 133-138.
Miller, L. J., and R. G. Strauch, 1974: A dual-Doppler radar method for the determination of wind velocities within precipitating weather systems. Remote Sens. Environ., 3, 219-235.
Ray, P. S., C. L. Ziegler, W. Bumgarner and R. J. Serafin, 1980: Single and multiple Doppler radar observations of tornadic storms. Mon. Wea. Rev., 108, 1607-1625
Ziegler, C. L., 1978: A dual-Doppler variational objective analysis as applied to studies of convective storms. Master’s thesis, University of Oklahoma, 115 pp.

## Slide 12: Supplementary Slides
Coplane retrieval of airborne
radial velocities for Hurricane Katrina (2005)

## Slide 13: What our group does now… P-3 Super Observation
(Weng and Zhang 2012)
Methodology
  Separate forward/backward sweeps
  Generate a volume by combining forward (or backward) scans within 1 minute
  Divide volume into smaller bins
  Observation selection and additional quality control of each observation and bin
  Generate SO value and radar relative location
  Data thinning, random sorting, and innovation thresholds.
One Volume
Notes: Sweep splitting done on each leg. Based on earth relative elevation from horizon. P-3 scanning switches back and forth at top of scanning.
Translation < 5.6 km when scanning; 5 scans in each volume
Each bin has length 5km, azimuth 5o, and thus 5 bins per radial direction.
QC:
  Raw observations < 2 m s-1 (inseparable from radar noise) and > 70 m s-1 (larger than maximum unambiguous radial velocity for PRT technique). Remove raw observations within 4 km of radar.
  Remove observations if (obs_Vr - bin_mean_Vr) > 2 STDEV bin. Reduce spread of bin.
  Remove bin if bin_STDEV > volume_STDEV
  Remove bin if < 4 valid raw observations
SO is the median value of bin with observation closest to bin center used for bin location.

## Slide 14: Flight Leg 1900-1946

## Slide 15
RMSEstarboard = 10.26 m s-1
RMSEport = 11.61 m s-1
[m s-1]
Flight Leg 1900-1946
Coplane Retrieval
Dual Doppler

## Slide 16: Flight Leg 2209-2253

## Slide 17
RMSEstarboard = 4.47 m s-1
RMSEport = 5.50 m s-1
[m s-1]
Flight Leg 2209-2253
Coplane Retrieval
Dual Doppler