## Slide 1: All-Sky Fast Radiative Transfer Modeling in the Microwave: Advancing the CRTM to Microphysics-Consistent Cloud Optical Properties
Research Group Meeting
11 December 2015
Scott Sieron
Advisor: Fuqing Zhang
Major Collaborators: Eugene Clothiaux, Lu Yinghui

## Slide 2
COLD
WARM
Hurricane Karl 09/16/10 2315Z
(GOES-13 IR, image courtesy NRL)
Hurricane Karl 09/16/10 2315Z
(GOES-13 VIS, image courtesy NRL)
Infrared
Visible (near sunset)
Brightness Temperature (K)
190
210
230
250
270
290
Notes: I’m sure that many of us are familiar with these sorts of representations of tropical cyclones, namely the visible and infrared as viewed from satellites. These images certainly demonstrate the existence of the storm, and provide some qualitative sense of storm intensity, but there is little direct evidence or signal from what is present below cloud top.
The visible image is produced by scattered sunlight, while the signal at this IR frequency is produced mostly by the emission from the highest altitude solids and liquids and is indicative of their temperature.

## Slide 3
Hurricane Karl 09/17/10 0113Z
(SSMI/S image courtesy NRL)
Hurricane Karl 09/17/10 0113Z
(SSMI/S image courtesy NRL)
High-mid microwave freq. (91.7 GHz)
Low-mid microwave freq. (37 GHz)
COLD
WARM
Brightness Temperature (K)
190
210
230
250
270
COLD
WARM
Brightness Temperature (K)
160
180
220
240
260
200
Notes: In contrast, shown here are perhaps less familiar representations of tropical cyclones, these are satellite images of brightness temperature in the microwave spectrum. This is of the same hurricane at nearly the same time as the previous two images. In these passive microwave observations, there is much more direct evidence of what exists below cloud top, which can be very useful information.
In both images, the hurricane looks substantially different than, for example the area of cloudiness to the north. The right image is even more substantially different, having greater contrast within the area of the hurricane, and an evident eye-like structure; in fact, it is the eye.
Clear-air 37 GHz over ocean has low brightness temperature because surface has low emissivity, it’s emitting far less radiation at this frequency than would a “perfect” black body emitter. The land has high emissivity, it has high brightness temperature.
Warm anomalies in 37 GHz brightness temperature over ocean is liquid cloud and rain. Liquid drops have fairly high emissivity and net adds to the radiance. It also absorbs some of what the surface emits, but clearly it emits more than it absorbs.
  There is substantial dynamic range within observable liquid hydrometeor content: the warmer it is, the more liquid hydrometeors there are. Observe that the heavy rain of the tropical cyclone (and convection south of Mexico) is substantially warmer than cloudy areas elsewhere.
Clear-air 91 GHz are warm both over water and land, and low brightness temperature anomalies are present over both. This is the precipitation-size ice particles (snow, graupel and hail) scattering

## Slide 4: Background: Passive Microwave Observations
At higher frequencies (> ~50 GHz),
  Surface has high emissivity (high brightness temperatures in clear air)
  Primary hydrometeor impact: reduction of radiance due to scattering by precipitation ice (snow, graupel, hail)
OCEAN
ATMOSPHERE
Planck function radiance (surface temperature)
Actual radiance
Notes: - Lower brightness temperature corresponds to more and larger precipitation ice

## Slide 5: Background: Passive Microwave Observations
OCEAN
ATMOSPHERE
Planck function radiance (surface temperature)
Actual radiance
At lower frequencies (< ~50 GHz) over water,
  Surface has low emissivity (low brightness temperatures in clear air) in H-polarization
  Primary hydrometeor impact: net addition of radiance due to absorption/emission by cloud and rain
Notes: - Higher brightness temperature corresponds to more mass of liquid hydrometeors

## Slide 6: Background: Passive Microwave Observations
At lower frequencies (< ~50 GHz) over water,
  Surface has low emissivity (low brightness temperatures in clear air) in H-polarization
  Primary hydrometeor impact: net addition of radiance due to absorption/emission by cloud and rain
  (Great numbers of large ice particles will produce meaningful scattering)
OCEAN
ATMOSPHERE
Planck function radiance (surface temperature)
Actual radiance

## Slide 7
Hurricane Karl 09/17/10 0113Z
(SSMI/S image courtesy NRL)
Hurricane Karl 09/17/10 0113Z
(SSMI/S image courtesy NRL)
High-mid microwave freq. (91.7 GHz)
Low-mid microwave freq. (37 GHz)
Clear air
Cloud
Rain
Heavy Rain,
Precip Ice
COLD
WARM
Brightness Temperature (K)
160
180
220
240
260
200
COLD
Brightness Temperature (K)
190
210
230
250
270
WARM
Notes: Using observations at substantially different frequencies can be especially powerful.
At lower frequencies such as 37 GHz, over locations of water surface, higher brightness temperatures correspond to more cloud liquid and rain present, but it is largely ambiguous as to the presence of ice particles. A higher frequency observation, such as 91.7 GHz, is sensitive to this.
At higher frequencies such as 91.7 GHz, warmer temperatures (shown in blue) correspond to lack of ice particles, but it is ambiguous as to the presence of some low-altitude liquid cloud. The lower-frequency observation is sensitive to this.
Clear-air 37 GHz over ocean has low brightness temperature because surface has low emissivity, it’s emitting far less radiation at this frequency than would a “perfect” black body emitter. The land has high emissivity, it has high brightness temperature.
Warm anomalies in 37 GHz brightness temperature over ocean is liquid cloud and rain. Liquid drops have fairly high emissivity and net adds to the radiance. It also absorbs some of what the surface emits, but clearly it emits more than it absorbs.
  There is substantial dynamic range within observable liquid hydrometeor content: the warmer it is, the more liquid hydrometeors there are. Observe that the heavy rain of the tropical cyclone (and convection south of Mexico) is substantially warmer than cloudy areas elsewhere.
Clear-air 91 GHz are warm both over water and land, and low brightness temperature anomalies are present over both. This is the precipitation-size ice particles (snow, graupel and hail) scattering

## Slide 8: Microwave Radiative Transfer and Frozen Hydrometeors
Hydrometeor size is critical:
  Up to [particle radius] ≈ ~1/6 wavelength: scattering increases by ~[particle mass]2
    Rayleigh scattering of a homogenous sphere
  Beyond [particle radius] ≈ ~1/6 wavelength: mass scattering coefficient grows more slowly, oscillates, then declines
    Mie scattering of a homogenous sphere
Largest precipitation particles exceed Rayleigh scattering size regime
Mass extinction (thick solid), scattering (dashed) and absorption (thin solid) coefficients (m2 g-1) of solid ice spheres as a function of radius for three imaging channels. Wavelength and 1/6-wavelength demarked.

## Slide 9: Community Radiative Transfer Model (CRTM)
A radiative transfer forward model simulates the radiance that would be measured by a specified sensor under specified atmospheric and surface conditions
The CRTM represents hydrometeor particle sizes with an effective radius parameter
  The calculation of an effective radius from a particle size distribution is non-trivial when the sizes of some particles exceed the Rayleigh scattering regime
  The CRTM effective radius parameter is representative of some unknown, specific particle size distribution which may or may not match that of the intended CRTM input

## Slide 10: Research Questions
Can the CRTM be modified to accurately represent the radiance impacts of hydrometeors produced by regional-scale NWP microphysics (MP) schemes?
  The CRTM is important: used for operational data assimilation of radiance measurements in clear- and cloud-sky conditions
If yes, then how do the results of the modified CRTM compare to observations?

## Slide 11: Modifying the CRTM for All-sky Microwave
Create new cloud optical property lookup tables
  Model the properties of single particles (soft spheres, as specified by MP scheme)
    Maxwell-Garnett mixing formula for ice dielectric constants
    Liquid dielectric constants from Tuner et al. (in prep)
    Product of the Henyey-Greenstein and Rayleigh scattering phase functions, and Legendre coefficients thereof, as specified by Liu and Weng (2006)
  Calculate per-mass optical properties of clouds constructed with particles with size distribution as specified by MP scheme
Lookup table dimensions match MP scheme output variables
MP scheme will be directly interfaced with CRTM
Notes:   Though both the MP schemes and CRTM remain sources for error/bias to observation

## Slide 12: Microphysics Scheme Details, Example
WSM6 Graupel
Exponential PSD:
    Based on Houze et al. (1979)
Soft sphere, ρg = 500 kg m-3
Dimensions of the CRTM lookup table (2): ρaqg, microwave frequency
Chart: Particle SIze (microns)
| 0 | 62.5 | 125 | 250 | 500 | 1000 | 2000
Exponential Distribution | 4 | 3.3161 | 2.7492 | 1.8895 | 0.89252 | 0.19915 | 0.009915
Mean of Distribution | 0 | 6
WSM6 Graupel PSD for = 3000 m-1

## Slide 13
Observations (SSMI/S)
100
140
180
220
260
300
Brightness Temperature (K)
96W
95W
94W
93W
92W
91W
97W
96W
95W
94W
93W
92W
91W
97W
Obs 37 GHz
Obs 91.7 GHz
17N
18N
19N
20N
21N
22N
23N
17N
18N
19N
20N
21N
22N
23N

## Slide 14
WSM6 Microphysics,
New Lookup Table
100
140
180
220
260
300
Brightness Temperature (K)
CRTM 36.5 GHz
CRTM 89 GHz
Obs. 37 GHz
17N
18N
19N
20N
21N
22N
23N
96W
95W
94W
93W
92W
91W
97W
96W
95W
94W
93W
92W
91W
97W
17N
18N
19N
20N
21N
22N
23N
Obs. 91.7 GHz
Notes: - This and the other CRTM results to follow are from the output of a 3-hour simulation using the WRF-ARW model at a 3 km grid. All of the simulations are of identical setup, initial and boundary conditions, differing only in the microphysics scheme.

## Slide 15
Morrison Microphysics,
New Lookup Table
100
140
180
220
260
300
Brightness Temperature (K)
CRTM 36.5 GHz
CRTM 89 GHz
17N
18N
19N
20N
21N
22N
23N
96W
95W
94W
93W
92W
91W
97W
96W
95W
94W
93W
92W
91W
97W
17N
18N
19N
20N
21N
22N
23N
Obs. 37 GHz
Obs. 91.7 GHz
Notes: - This and the other CRTM results are from the output of a 3-hour simulation using the WRF-ARW model at a 3 km grid. All of the simulations are of identical setup, initial and boundary conditions, differing only in the microphysics scheme.

## Slide 16
Goddard Microphysics,
New Lookup Table
100
140
180
220
260
300
Brightness Temperature (K)
CRTM 36.5 GHz
CRTM 89 GHz
17N
18N
19N
20N
21N
22N
23N
96W
95W
94W
93W
92W
91W
97W
96W
95W
94W
93W
92W
91W
97W
17N
18N
19N
20N
21N
22N
23N
Obs. 37 GHz
Obs. 91.7 GHz
Notes: - This and the other CRTM results are from the output of a 3-hour simulation using the WRF-ARW model at a 3 km grid. All of the simulations are of identical setup, initial and boundary conditions, differing only in the microphysics scheme.

## Slide 17
CRTM TB (K) 36.5-H GHz, Only Cloud Liquid, Rain and Snow
WSM6
Morrison
Snow
Snow particle concentration (Log10 #/kg), height vs. particle size in the storm area
0
20
40
60
80
100
120
-6
-4
2
0
2
4
6
Snow water path (g m-2)
100
140
180
220
260
300
Storm area average: 11.9 g m-2
Storm area average: 19.7 g m-2

## Slide 18
CRTM TB (K) 36.5-H GHz, Only Cloud Liquid, Rain and Graupel
WSM6
Graupel
Graupel particle concentration (Log10 #/kg), height vs. particle size in the storm area
0
50
100
150
200
250
-6
-5
-4
-3
-2
-1
0
1
2
3
Morrison
Graupel water path (g m-2)
100
140
180
220
260
300
Storm area average: 8.6 g m-2
Storm area average: 7.1 g m-2

## Slide 19: Results and Discussion
Using scheme-specified cloud optical properties: too low of brightness temperatures, too much scattering
  Consistent with many studies involving radar and passive microwave observations vs. simulated [Zupanski et al. 2011; Zhang et al. 2013; Han et al. 2013; Chambon et al. 2014]
  These studies used the Goddard-SDSU radiative transfer solver
Conclusion: too much or too big of snow and/or graupel in upper troposphere by microphysics schemes

## Slide 20: Future Directions
Refining and adding modifications, working within the CRTM repository
  Non-spherical particle optical properties
  Automatic stream number estimation
  Revamp data structures, scheme selection interface
  Tangent linear, adjoint, K-matrix
  Antenna pattern convolution and slant path constructions (features in satellite simulators)
Uses for this tool:
  Ensemble parameter estimation
  Observing System Experiments (testing data assimilation)
    Simulated or real observations

## Slide 21: References
Chambon, P., S. Q. Zhang, A. Y. Hou, M. Zupanski, and S. Cheung, 2014: Assessing the impact of pre-GPM microwave precipitation observations in the Goddard WRF ensemble data assimilation system. Quart. Jour. Roy. Meteor. Soc., 140, 1219–1235.
Han, M., S. A. Braun, T. Matsui, and C. R. Williams, 2013: Evaluation of cloud microphysics schemes in simulations of a winter storm using radar and radiometer measurements. J. Geophys. Res. Atmos., 118, 1401–1419.
Liu, Q., and F. Weng, 2006: Advanced doubling-adding method for radiative transfer in planetary atmospheres. J. Atmos. Sci., 63, 3459‒3465.
Skamarock, W. C., J. B. Klemp, J. Dudhia, D. O. Gill, D. M. Barker, M. G. Duda, X.-Y. Huang, W. Wang, and J. G. Powers, 2008: A description of the Advanced Research WRF version 3. NCAR Technical Note 475, http://www.mmm.ucar.edu/wrf/users/docs/arw_v3.pdf.
Weng, Y., and F. Zhang, 2012: Assimilating Airborne Doppler Radar Observations with an Ensemble Kalman Filter for Convection-permitting Hurricane Initialization and Prediction: Katrina (2005). Mon. Wea. Rev., 140, 841-859.
Wong, V., and K. A. Emanuel, 2007: Use of cloud radars and radiometers for tropical cyclone intensity estimation, Geophys. Res. Lett., 34, L12811, doi:10.1029/2007GL029960.
Zhang, S. Q., M. Zupanski, A. Y. Hou, X. Lin, and S. H. Cheung, 2013: Assimilation of Precipitation-Affected Radiances in a Cloud-Resolving WRF Ensemble Data Assimilation System. Mon. Wea. Rev.,141, 754–772.
Zhang, F., Y. Weng, J. A. Sippel, Z. Meng, and C. H. Bishop, 2009: Cloud-resolving Hurricane Initialization and Prediction through Assimilation of Doppler Radar Observations with an Ensemble Kalman Filter. Mon. Wea. Rev., 137, 2105-2125.
Zupanski, D., S. Q. Zhang, M. Zupanski, A. Y. Hou, and S. H. Cheung, 2011: A Prototype WRF-Based Ensemble Data Assimilation System for Dynamically Downscaling Satellite Precipitation Observations. J. Hydrometeor., 12, 118–134.

## Slide 22: Extra Slides

## Slide 23: WSM6, New Look-up Tables Coarsened to 15x15 km
89 GHz
36.5 GHz

## Slide 24: WSM6, New Look-up Tables
89 GHz
36.5 GHz

## Slide 25: WSM6, Specified and Uniform CRTM Radii
Cloud: 15 μm Rain: 500 μm Ice: 50 μm Snow: 1000 μm Graupel: 1000 μm
80
100
120
140
160
180
200
220
240
260
280
300
Brightness Temperature (K)

## Slide 26
WSM6
10.65-H
18.7-H
23.8-V
36.5-H
89.0-H
165.5-H