## Slide 1: Ozone Sensitivity to Nitric Oxide Emissions in WRF-Chem
ADAPT meeting- Summer 2016
Andrew Thomas
Advisers: Amy Huff and Fuqing Zhang

## Slide 2: Nox Sensitivity tests
O3 is a secondary pollutant, from which NO2 is one precursor chemical.
NOx emissions contain many uncertainties and are updated once every few years.
NEI-2011 Emissions
NEI-2011 Emissions with 20% less anthropogenic NOx
NEI-2011 Emissions with 20% more anthropogenic NOx
NEI-2005 Emissions
Notes: earlier

## Slide 3: O3 and human health
Ozone is considered by the EPA as one of the 6 “criteria pollutants.”
Ozone is inhaled and it oxidizes the mucus membrane lining of the lung
Inhaled ozone oxidizes the lining of the lungs, causing a “reactive cascade” which leads to cardiovascular problems.
Air Quality Index Levels of Health Concern | Maximum 8 Hour Average Ozone Level | Meaning
Good | 0-55 ppb | Air quality is considered satisfactory, and air pollution poses little or no risk.
Moderate | 55-71 ppb | Air quality is acceptable; however, for some pollutants there may be a moderate health concern for a very small number of people who are unusually sensitive to air pollution.
Unhealthy for Sensitive Groups | 71-86 ppb | Members of sensitive groups may experience health effects. The general public is not likely to be affected.
Unhealthy | 86-106 ppb | Everyone may begin to experience health effects; members of sensitive groups may experience more serious health effects.
Very Unhealthy | 106-201 ppb | Health warnings of emergency conditions. The entire population is more likely to be affected.
Hazardous | >201 ppb | Health alert: everyone may experience more serious health effects.

## Slide 4: Background: O3 and NOx
Ozone formed from oxygen atom and oxygen molecule.
Oxygen molecule formed from the photolization (reaction with UV radiation) of NO2
NO2 formed via NO and CH3O2
Notes: Fewer eqns

## Slide 5: The model: WRF-Chem
Offline Air Quality Models (like CMAQ)
Computes chemistry after meteorology
Computationally inexpensive
Used operationally and for regulatory purposes
Often interpolates between chemistry grid and meteorology grid.
Online Air Quality Models (like WRF-Chem)
Computes chemistry concurrently with meteorology
Computationally more expensive
Used experimentally
Has the potential to allow chemistry to affect meteorology.

## Slide 6: ‘Control’ Model Setup
Chemistry
  RACM
Photolysis
  Madronich
Biogenic Emissions
  MEGAN
Anthropogenic Emissions
  NEI-2011
Chemical Boundary Conditions
  MOZART
Cumulus Physics
  Grell-Devenyi
Radiation
  Dudhia (SW) and RRTM (LW)
Microphysics
  WSM6
Boundary Layer
  YSU
Boundary and Initial Conditions
  GFS, cycled every 24 hours
Model spun up for two days prior to analysis

## Slide 7: Description of event:
Model spun up from 9/13/15 12:00 UTC – 9/15/15 12:00 UTC
Model ran from 9/15/15 12:00 UTC – 9/21/15 12:00 UTC
Peak event occurred 9/16/15 – 9/18/15 UTC
  One of the few periods with multiday high ozone event

## Slide 8: Verification of ‘Control’ Model over event

## Slide 9: Verification of ‘Control’ Model over event

## Slide 10: Verification of ‘Control’ Model over event

## Slide 11: Nox Sensitivities of nEI-11: NOx

## Slide 12: Nox Sensitivities of nEI-11: O3

## Slide 13: Nox Sensitivity: Reduction comparison
Average Hourly O3 from 9/17/15 12 UTC to 9/18/15 12 UTC
Notes: Fix colorbars
Remove suptitle

## Slide 14: Nox Sensitivity: Increase comparison
Average Hourly O3 from 9/17/15 12 UTC to 9/18/15 12 UTC

## Slide 15: NEI 2011 and NEI 2005

## Slide 16: NEI 2005 – NEI 2011 Comparison
Average Hourly O3 from 9/17/15 12 UTC to 9/18/15 12 UTC

## Slide 17: Conclusions
This is still an early result
There may be more at work with the other pollutants. The change in ozone from changing only the NOx is smaller than expected.
Ozone during the day seems to be more sensitive to NOx emissions than ozone in the evening.
Despite being a secondary pollutant, WRF-Chem produces better O3 forecasts than NOx forecasts
  There may be a bias here- NOx monitors are usually sparser than O3 monitors and found in urban areas.

## Slide 18
O3
NOx
Notes: Separate plots
Limit to 17th

## Slide 19: Background: O3 and Simplified Nonlinear relationship to NOx
From Meteo 419, year 2014, lecture 15

## Slide 20: Background: Human Health and Ozone
Notes: No fig
Bring in communication and modelling bqckg

## Slide 21: ‘Control’ Model Setup
Setting | Name
Chemistry | Regional Atmospheric Chemical Mechanism (RACM) with Kinetic Preprocessor (KPP)
Photolysis | Madronich
Biogenic Emissions | Model of Emission of Gases and Aerosols from Nature (MEGAN)
Anthropogenic Emissions | National Emissions Inventory 2011 (NEI-2011)
Chemical Boundary Conditions | Model of Ozone and Related Tracers (MOZART)
Resolution | 12 km with 159 gridpoints, 44 vertical levels
Boundary Layer | Yonsei State University (YSU)
Cumulus | Grell-Devenyi
Microphysics | WRF Single Moment 6 class (WSM6)
Meteorological initial and Boundary Conditions | Global Forecasting System (GFS) refreshed every 24 hours. Two day spin-up (not shown).
Radiation | Dudhia (shortwave) and RRTM (longwave)
Notes: Bullets

## Slide 22
Description of Test event: Sept. 15th 2015: Beginning
Notes: Less meteo

## Slide 23: Description of Test event: Sept. 17th 2015: Peak
Lee Trough

## Slide 24: Description of Test event: Sept. 21st, 2015: End